## Slide 1: NANOG 76
HACKATHON
Syed Ahmed
Deepak Padliya
{syed.w.ahmed,deepak.padliya}@oracle.com

## Slide 2
Endpoint A
Endpoint B
Endpoint A
Endpoint B
Endpoint A
Endpoint B
Healthy State
Failure
Repaired

## Slide 4: Active Monitoring

## Slide 5: Agenda
Problem Statement
Goals
Topology Overview
BGP-LS Overview
Networkx
IP GRE Encap/Decap
Exabgp (parser)
Scapy Overview
jq Overview
Visualization - InfluxDB and Grafana

## Slide 7: Problem Statement
Mechanisms/tools to identify failures in dense and complicated network
Active monitoring sensors/agents
  End-to-end reachability
  Packet loss
  Latency across the network
Topologies with multiple active paths require increased complexity to ensure coverage of all possible path segments

## Slide 8: Problem Statement
Possible best paths between Host A to B in steady state if all links have same cost:
  r1-r2-r4-r6
  r1-r2-r5-r6
  r1-r3-r5-r6
  r1-r3-r4-r6
In order to make sure that network is in healthy state, test traffic should take all possible path segments from host A to B

## Slide 9: Hackathon Goals
Extract topology information
Build network graph with nodes, links and metrics
Use network graph to compute all best possible paths between two end points
Construct probe packets
Probe all calculated paths
Introduce and account for failure
Bonus
  Visualize collected data/metric

## Slide 10: Topology Overview
Six device topology using Juniper VMXs
Two ubuntu based Linux hosts connected to R1 and R6.
IS-IS as IGP (feel free to change it to your choice of IGP)
R1 and R6 has BGP-LS configured
  ASN: 65535
On host you can run exabgp with R1 or R6 to get BGP-LS info (more on that later)
Notes: Change asn to something else as 65535 is reserved

## Slide 11: BGP-LS
BGP-LS is another NLRI of BGP
It uses BGP TLVs to define Objects
  Nodes
  Links
  IP Prefixes
Node Attributes
  Node Name
  Router-ID
  Multi-Topology identifier (etc.)
Links Attributes
  Local IP
  Remote IP
  Local and Remote Router ID
  Max Bandwidth (etc.)
IP Prefix
  Protocol ID
  Local Node descriptor
  Prefix Descriptor

## Slide 12: BGP-LS (what that actually means)
Collecting Link-State and Traffic Engineering information from IGPs (IS-IS or OSPF) and sharing with external entities using BGP

## Slide 13: BGP-LS (Node)
Node LS
Router ID
Hostname

## Slide 14: BGP-LS (LINK)
Local IP
Remote IP
Metric
Link LS

## Slide 15: Exabgp Support
Script to parse update
BGP-LS address family on exabgp
Message types to parse

## Slide 16: Message Format
Router ID
Router Name
Options for JSON parsing to glean nodes and links:
Write your own code in programming language of your choice.
Use jq (discussed later).

## Slide 17: NetworkX
Most languages have Graph libraries like:
  Python  NetworkX, iGraph
  GoLang  Goraph
>>> import networkx
>>> g = networkx.Graph()
>>> g.add_node("R1")
>>> g.add_node("R2")
>>> g.add_node("R3")
>>> g.add_edge("R1", "R3")
>>> g.add_edge("R1", "R2")
>>> g.add_edge("R2”,"R3")
>>> print g.number_of_nodes() 3
>>> print g.number_of_edges() 3
>>> print g.nodes() ['R1','R2','R3']
Import library
Create new undirected graph
Add new nodes with unique IDs.
Add new edges referencing associated node IDs.
Print details of our newly- created graph.
Sample Graph

## Slide 18: IP GRE Encap/Decap
Encapsulate a packet with new outer IP header (source and dest)
After de-encapsulating outer GRE header packet is forward based on inner header
In context of our use-case we are using stateless GRE
Notes: Config snippet to decap gre decap.

## Slide 19
SCAPY (discussed next) can be used for Packet construction and manipulation.
IP
GRE
IP
GRE
IP
Payload
20.0.0.2
GRE
10.0.0.1
20.0.0.2
GRE
10.1.1.1
Payload
20.0.0.2
20.0.0.2
Outer Header
Inner Header
Outer Header
Inner Header

## Slide 20: Scapy Overview
Scapy is a free (GPLv2) , powerful interactive packet manipulation tool written in Python
Enables the user to send, sniff , dissect and forge network packets
Allows construction of tools that can probe, scan or attack networks
Easily handles tasks like network discovery , scanning, tracerouting and probing
Runs as an interactive shell or can be imported into a python script

## Slide 21: Scapy - Sending & Receiving a Ping packet

## Slide 22: Scapy – Sending & Receiving Multiple Ping Packets

## Slide 23: jq Overview
JQ is a lightweight and flexible command-line JSON processor
Like sed for JSON data - you can use it to slice , filter , map, transform structured data with the same ease that sed, awk, grep lets you do with text
jq is written in portable C, and it has zero runtime dependencies. You can download a single binary for Linux, OS X and Windows

## Slide 24: jq – Example Input Data
lab@vmx19-1> show isis adjacency detail
vmx19-1-1
Interface: ae0.0, Level: 2, State: Up, Expires in 21 secs
Priority: 0, Up/Down transitions: 1, Last transition: 04:42:18 ago
Circuit type: 2, Speaks: IP, IPv6
Topologies: Unicast
Restart capable: Yes, Adjacency advertisement: Advertise
IP addresses: 1.1.1.1
Level 2 IPv4 Adj-SID: 17
xrv6-5-1
Interface: ae1.0, Level: 2, State: Up, Expires in 22 secs
Priority: 0, Up/Down transitions: 1, Last transition: 17:32:54 ago
Circuit type: 2, Speaks: IP
Topologies: Unicast
Restart capable: Yes, Adjacency advertisement: Advertise
IP addresses: 1.1.1.5
Level 2 IPv4 Adj-SID: 16
Notes: What is jq is used for give a brief overview.

## Slide 25: jq - Understanding JSON Schema
jq '.[][0].attributes.xmlns'
.[] returns each element of the array returned in the response, one at a time

## Slide 26: jq- JSON Path to jq Command
jq '.[][0]."isis-adjacency"[0]."interface-name"[0].data'

## Slide 27: Jq - Filter/Select Example
jq '.[][0]."isis-adjacency"[]| select(."interface-name"[0].data=="ae0.0")'

## Slide 28: jq - Custom JSON Output
jq '.[][0]."isis-adjacency"[]| select(."interface-name"[0].data=="ae0.0") | {system_name: ."system-name"[0].data, interface_name: ."interface-name"[0].data}'

## Slide 29: jq - CSV Creation(One Interface Only)
jq --raw-output '.[][0]."isis-adjacency"[]| select(."interface-name"[0].data=="ae0.0") | {system_name: ."system-name"[0].data, interface_name: ."interface-name"[0].data} | [."system_name", ."interface_name"]|@csv’
Precede jq command with echo “system-name,interface-name”; to print CSV header

## Slide 30: jq - Csv Creation(All Interfaces)
jq --raw-output '.[][0]."isis-adjacency"[]| {system_name: ."system-name"[0].data, interface_name: ."interface-name"[0].data} | [."system_name", ."interface_name"]|@csv'

## Slide 31: Grafana and InfluxDB Overview
Grafana is an open source, feature rich metrics dashboard and graph editor for InfluxDB, Graphite, Elasticsearch, OpenTSDB and Prometheus
InfluxDB is an open-source time series database (TSDB) developed by InfluxData

## Slide 32: InfluxDB and Grafana
Grafana
http API

## Slide 33: Inserting Data Into InfluxDB
rtt.txt
=====
# DDL
CREATE DATABASE rtt
# DML
# CONTEXT-DATABASE: rtt
probe probe=0,time_rtt=84.85,seq=0 1557262142950442240
probe probe=0,time_rtt=19.23,seq=1 1557262143030176000
probe probe=0,time_rtt=24.01,seq=2 1557262143049575936
probe probe=0,time_rtt=16.22,seq=3 1557262143072866816
:
$ influx -import -path=rtt.txt -precision=ns
2019/05/07 17:54:41 Processed 1 commands
2019/05/07 17:54:41 Processed 200 inserts
2019/05/07 17:54:41 Failed 0 inserts

## Slide 34: Creating Grafana Dashboard

## Slide 35: Creating Grafana Dashboard

## Slide 36: Creating Grafana Dashboard

## Slide 37: Creating Grafana Dashboard

## Slide 39: Special Thanks to our Lab Partner

## Slide 41: Useful Links
Scapy Cheat Sheet
  https://blogs.sans.org/pen-testing/files/2016/04/ScapyCheatSheet_v0.2.pdf
Jq Playground
  https://jqplay.org/
Jq Tutorial
  https://programminghistorian.org/en/lessons/json-and-jq
Grafana Getting Started
  https://grafana.com/docs/guides/getting_started
Git Repo
  https://github.com/swahmed-nanog/nanog76_hackathon
Yaml Parser
  https://yaml-online-parser.appspot.com/

## Slide 42: SCAPY – Sending & Receiving IP/GRE/IP/UDP Packet